## Slide 1
Spatial Data Focusing:
An alternative to Beamforming for geocasting scenarios
GEOHYPE project
ANR funding - JCJC program
Julien Sarrazin, Michael Odhiambo
Sidney Golstein, Philippe De Doncker, François Horlin

## Slide 2: GEOcasting for HYPEr resolution spatial data focusing
Goal: Wireless broadcasting of geolocalized data
Applications:
  Interactive contents in museums
  Danger areas indication for visual impaired persons (zebra crossings…)
  Alert people within an area of sudden emergency
GEOHYPE system does not know users location
  User privacy is respected
  Lighter infrastructure

## Slide 3
Phased array: power focusing
Broadcasting
The data is being send to the location, whether a user is there or not
Power focusing
Physical limitation: beamwidth is related to aperture size of the array

## Slide 4
Spatial Data Focusing instead of power focusing

## Slide 5: Spatial Data Focusing
Principle

## Slide 6: Spatial Data Focusing
Example of a
2 antennas - 2D scenario
using IQ resources
- Simulations -

## Slide 7: Spatial Data Focusing
Example of Spatial Data Focusing: 2D IQ scenario
MISO configuration:
- Dual-antenna @ TX
- Single antenna @ RX
I
Q
θ=4°
θ=0°
θ=16°

## Slide 8: Spatial Data Focusing
Example of Spatial Data Focusing: 2D IQ scenario
3 concomitant effects can be observed:
The correct yI[k] amplitude is affected by a factor f(Δτ/2)cos π fc Δτ
Influence of Inter-Symbol-Interferences (ISI)
The projection of the symbol on the Q dimension is not perfect and therefore, part of the energy will be found onto the I dimension
Received kth estimated symbol (I projection only):
I
Q

## Slide 9: Spatial Data Focusing: 2D IQ scenario
Focusing effect: BER = f(θ)
16-QAM, f = 2.4 GHz, fd = 20 MHz, b = 0.8 λ, SNR = 20 dB (perfect synchronization)
Beamwidth @ BER = 10-3
BF:
Δθ = 51°
SDF:
Δθ = 6.3°

## Slide 10: Spatial Data Focusing
Example of a
N antennas – ND scenario - Simulation -

## Slide 11: Spatial Data Focusing
N dimensions
  N pulses orthogonal in time
  N orthogonal codes
  N orthogonal subcarriers
  …

## Slide 12: Spatial Data Focusing
3-dimension mapping
*
*
*
Front-End
Front-End
Front-End
Φ1
Φ2
Φ3
N PAM modulations
1 per antenna

## Slide 13: Spatial Data Focusing
BER results: comparison between power and data focusing
f = 2.4 GHz, fd = 20 MHz, b = 0.8 λ, M = 16 for N = 2, M = 64 for N= 3 (perfect synchronization)
Beamwidth @ BER = 10-3
BF using 16QAM:
Δθ = 51° (N = 2)
Δθ = 31° (N = 3)
SDF:
Δθ = 24° (N = 2)
Δθ = 12.5°(N = 3)

## Slide 14: Spatial Data Focusing
6-dimension mapping
*
*
*
Front-End
Front-End
Front-End
N QAM modulations
1 per antenna
Use time resources:
  N orthogonal pulses
Use IQ resources:
  2N dimensions
N antennas and 2N dimensions

## Slide 15: Spatial Data Focusing
BER results: comparison between power and data focusing (with channel estimation)
N = 2 antennas - 4 dimensions (I1+jQ1 & I2+jQ2)
N = 3 antennas - 6 dimensions (I1+jQ1 & I2+jQ2 & I3+jQ3)
Beamwidth @ BER = 10-3
BF:
Δθ = 51°(N = 2)
Δθ = 31°(N = 3)
SDF:
Δθ = 3.3°(N = 2)
Δθ = 1.8°(N = 3)
Notes: SNR = 20dB
Channel assumed constant during the frame

## Slide 16: Spatial Data Focusing
Example of a
2 antennas - 4D scenario
- Measurements -

## Slide 17: Spatial Data Focusing
Measurement Setup
AWG (2 x 12 GSa/s)
Scope (40 GSa/s)

## Slide 18: Spatial Data Focusing
Measurement Results
N = 2 antennas - 4 dimensions (I1+jQ1 & I2+jQ2)
Beamwidth @ BER = 10-3
SDF:
Δθ = 17.4° (M = 16)
Δθ = 4.1° (M = 256)
Parameters
fc = 2.67 GHz
b = 0.8 λ
fd = 20 MHz
Noise robustness equivalence
M = 16  QPSK
M = 256  16QAM
1D = 1 bit
1D = 2 bits

## Slide 19: Spatial data focusing (SDF)
On-going
Orthogonal-code-based N-dimensions SDF
Orthogonal-frequency-based N-dimensions SDF
Channel assessment
More antennas:
Perspectives
Channel estimation and equalization
Carrier recovery
N-Dimension dedicated mapping
Protocol aspects
Looking for collaborations

## Slide 20: Channel EQ
θ = -32°
N = 2 antennas, 4 dimensions using orthogonal pulses and IQ resources
I1Q1
I2Q2
I1I2
Q1Q2
Channel estimation
Magnitude estimated on the 4D symbol
Phase estimated from the 2D of the 1st antenna
Notes: SNR = 20dB, N = 2

## Slide 21: Spatial Data Focusing: Constellation analysis
Example of Spatial Data Focusing: 2D IQ scenario
Distance between TX antennas: b = 0.75λ

## Slide 22: Spatial Data Focusing
SDF VS Beamforming: 16QAM
16.6°
5.6°